## Slide 1: Energy Hub (E-Hub) Modeling Tool v2.0 Introduction & Demonstration
Mashael Yazdanie
March 21, 2018

## Slide 2: Goals
Introduction of the E-Hub Tool
  What is it?
  Why use it?
  Scope and input parameters
  Limitations
Demonstration
  Getting started with the E-Hub Tool
  Configure input file, run model, view results
  Cases illustrating breadth of applications
Future development / your inputs

## Slide 3: What is the E-hub Modeling Tool?
An open source, bottom-up, energy system modeling and MILP optimization tool, suitable for representing a broad range of energy systems
Facilitates energy system capacity and dispatch (operation) planning
Provides users with the flexibility to define an energy hub as an interconnected system of self-described:
  energy carriers;
  energy conversion and distribution technologies (i.e., converters, storages, and network links); and
  energy demands
Single or multi-hub optimization

## Slide 4: Benefits of the E-hub Tool Approach
Easy to use:
  Intended to be easy to setup, learn and use for both experienced and novice energy system modelers
  Suitable for both “quick and dirty” modeling or more in-depth analyses
  Fast model setup through spreadsheet interface
  Intuitive and flexible navigation of results through (optional) spreadsheet interface
Flexible modeling framework:
  Energy systems can be defined to capture a wide range of scales and scopes (e.g., building level, neighborhoods, cities, cantons, etc.)
  A wide range of energy conversion, distribution and storage technologies can be defined by users
  Experienced users may define custom modules using Python/Pyomo
  Results are saved in a text file format which can be further processed

## Slide 5: Benefits of the E-hub Tool Approach
Ease of development:
  Python-based, open-source code
  Transparent documentation and code
  Open collaboration and development opportunities (vs. commercial software packages)

## Slide 6: Modeling Scope & Input Parameters Overview
Minimize cost or carbon emissions
Time scale: hourly
Specify any multi/single input/output energy conversion process which can be defined in terms of energy carrier streams and efficiencies
…optionally, specify:
  fixed input and/or output shares
  part-load efficiency
  pre-existing capacities
  caps on operation and capacity
  hourly solar insolation profile for solar technologies
Energy carrier tracking
Optional constraints on total carbon emissions and import supplies
Carbon emissions specifiable for energy carriers and tech installations
Capacity factors (annual and hourly)

## Slide 7: Modeling Scope & Input Parameters Overview
Hourly demand profiles for energy carriers
Network optimization (capacity planning and dispatch) based on defined connection layout; can also specify:
  uni/bi-directional flow connections
  networks for different energy carriers
  pre-existing capacities
  spatial information (connector length)
Costs considered:
  investment costs
  fixed/variable operation & maintenance costs
  energy carrier price (fixed or hourly)
  export price
  carbon taxes

## Slide 8: Current Limitations
Aimed at short-term time horizons
Fixed hourly time periods
Limited to energy technologies
Excel macro-enabled spreadsheet to view results capped at 1 million data rows (per worksheet)

## Slide 9: Getting Started
Download the latest version of the E-Hub Tool from GitHub:
https://github.com/hues-platform/python-ehub/tree/NextGen
Getting Started guide
Optimization problem formulation documentation
Input/output file templates
Demonstration cases
Requirements:
  Python 3.6+
  Python libraries: pandas, numpy, Pyomo
  Solver (e.g., gurobi, glpk)
  Spreadsheet editor (e.g., Microsoft Excel, OpenOffice)

## Slide 10: Single Hub
Imports
Exports
Energy system flow diagram

## Slide 11: Single Hub Energy System Flow Diagram

## Slide 12: Model Input File

## Slide 13: Running a Model

## Slide 14: Navigating Results

## Slide 15: Multi Hub
Imports
Exports
1
2
3

## Slide 16: Multi Hub + Network
Imports
Exports
3
1
2

## Slide 17: Multi Hub + Network + Centralized (Local) Generation
Imports
Exports
Generation hub
3
1
2
4

## Slide 18: Multi Hub + Network + Centralized (Local) Generation  Microgrid Operation
Imports
Exports
Microgrid
Generation hub
3
1
2
4

## Slide 19: Multi Hub - Communities
Imports/Exports

## Slide 20: Multi Hub - Countries
Imports/Exports

## Slide 21: Further Development
Adaptations providing modeling flexibility:
Flexible time period definitions (e.g., days, months, seasons, etc.)
Long-term (multi-year) planning
User interfacing (GUI, input error checking, etc.)
Model generation efficiency improvements
Integration with other models/research within UESL
…<insert your ideas>
Thank you!